## Slide 1: ADDING AND MODIFYING FF BLOCK OBJECTS

## Slide 2: Using Foundation Fieldbus Terms
Adding FF Variables – wrong
Adding FF Parameters – better
Adding FF Block Object – best!

## Slide 3: Process of Building FF Firmware

## Slide 4: FILES TO MODIFY
File Type | Extension | Present Implementation | Belongs to:
DDL file | .ddl | svi_positioner.ddl | DD side (SSDC)
Firmware DD script | .gw | SVI_Positioner_APP.gw | FF firmware script (Softing)
FW source code | .c | appl_ptb.c | FF firmware (Softing)
Files which we need to modify when working on insertion of new and modification of old parameters.

## Slide 5: Parameter Modification Work Flow

## Slide 6: TYPES OF PARAMETERS
By Periodicity of Addressing
- Cyclic high priority
- Cyclic low priority
- Non-cyclic
Structural Types
- Simple = VARIABLE
- Structure = RECORD

## Slide 7: DDL File Modifications
BLOCK PTB
{
CHARACTERISTICS ptb_character ;
LABEL LBL_POSITIONER_TRANSDUCER_BLOCK ;
HELP HLP_POSITIONER_TRANSDUCER_BLOCK ;
PARAMETERS
{
/* standard parameters */
ST_REV, __st_rev ;
TAG_DESC, __tag_desc ;
FINAL_VALUE, __final_value;
FINAL_POSITION_VALUE, __final_position_value;
.....other standard parameters....
...................................
/* non-standard parameters */
/* most likely here we are inserting new parameters */
CONTROL_PARAMETERS, svi_control_parameters_record;
FIND_STOPS, svi_find_stops;
SUPPLY_PRESSURE, svi_supply_pressure;
ACTUATOR_PRESSURE, svi_actuator_pressure;
RAMP_RATE, ramp_rate;
SLEEP, little_nap;
..........other non-standard parameters.... .....

## Slide 8: (continue from previous)
......................................
}
....other block components: vies, etc......
PARAMETER_LISTS
{
VIEW_1, ptb_view_1 ;
VIEW_2, ptb_view_2 ;
VIEW_3, ptb_view_3 ;
VIEW_4, ptb_view_4 ;
}
..............................................
..............................................
} /* end block definition */

## Slide 9: DD ITEMS
VARIABLE – simple
RECORD – structure, several components
Standard DD Item(with double underscore __)
Standard – do not define, but import files with definitions.
May be REDEFINE’d
Custom DD Item – needs to be defined

## Slide 10: Custom DD Items
Simple DD Item
VARIABLE ramp_rate
{
LABEL LBL_RAMP_RATE ;
HELP HLP_RAMP_RATE ;
CLASS CONTAINED ;
TYPE FLOAT ;
HANDLING READ & WRITE ;
}

## Slide 11: Custom DD Items (continued 1)
RECORD Type DD Item (Standard Members)
RECORD svi_supply_pressure
{
LABEL "svi_supply_pressure";
HELP "svi supply pressure";
MEMBERS
{
STATUS, __status_contained_nd ;
VALUE, __float_contained_nd ;
}
}

## Slide 12: Custom DD Items (continued 2)
Standard Members Definitions
Defined in file “std_parm.ddl”
Example:
VARIABLE __float_contained_nd
{
LABEL [value_label] ;
HELP [float_contained_help] ;
CLASS CONTAINED & OPERATE ;
TYPE FLOAT ;
HANDLING READ & WRITE ;
/* RESPONSE_CODES xxx ; */
}

## Slide 13: Custom DD Items (continued 2)
RECORD Type DD Item (Custom Members)
/**********************************************************************
little_nap
**********************************************************************
*/
VARIABLE time
{
LABEL "Sleep length" ;
HELP "Duration of snooze during this presentation in min." ;
CLASS CONTAINED ;
TYPE FLOAT ;
HANDLING READ & WRITE ;
}
VARIABLE uninterrupted
{
LABEL "Is uninterrupted" ;
HELP "True if your sleep uninterrupted all the way through" ;
CLASS CONTAINED ;
TYPE BOOLEAN ;
HANDLING READ & WRITE ;
}

## Slide 14: (continued from previous)
RECORD little_nap
{
LABEL "Nap quality" ;
HELP "Quality of your sleep during this meeting" ;
MEMBERS
{
LENGTH, time ;
QUALITY, uninterrupted;
}
}
/**********************************************************************/
Define all VARIABLEs (simple)
Define RECORD with these VARIABLEs

## Slide 15: VIEWs
VIEW_1
VIEW_2
VIEW_3
VIEW_4
Used for presentation of groups of parameters.
Grouping Principle: Dynamic vs. Static.
Creating VIEWs in DDL
VARIABLE_LIST ptb_view_1
{
LABEL LBL_PTB_VIEW_1 ;
HELP HLP_PTB_VIEW_1 ;
MEMBERS
{
VL_ST_REV, PARAM.ST_REV ;
VL_MODE_BLK, PARAM.MODE_BLK ;
VL_BLOCK_ERR, PARAM.BLOCK_ERR ;
..............................
}
}

## Slide 16: Object Redefinition
IMPORT MANUFACTURER __FF,
DEVICE_TYPE __STD_PARM,
DEVICE_REVISION SFT_STD_PARM_dev_rev,
DD_REVISION SFT_STD_PARM_dd_rev
{
EVERYTHING ;
REDEFINITIONS
{
REDEFINE VARIABLE __manufac_id
{
LABEL [manufac_id_label] ;
HELP [manufac_id_help] ;
CLASS CONTAINED ;
TYPE ENUMERATED (4)
{
{0x445644, "|en|Dresser Valve Division", [mfr_id_help]}
}
CONSTANT_UNIT [blank] ;
HANDLING READ ;
}
REDEFINE VARIABLE __dev_type
……………………………………………………………………….
Import standard object using the word “IMPORT”
Redefine it to you own need with the word “REDEFINE”.
For greater details reference DDL files

## Slide 17: Firmware DD Script
Most of our changes are to the file: <SVI_Positioner_APP.gw> in the
Softing codebase.
GW files define parameters of FF Blocks to help generating corresponding VFD blocks. VFD blocks are used in source code as regular C structures.
SCRIPT DEFINITION SEQUENCE (Parameter Descriptions)
Name same as in DDL file
Flags (such as Read/Write)
Length in bytes
Structure or simple variable type
(examples: Simple INTEGER32; Record FLOAT_S)
Number of components (such as number of Record members)
Initial values of all components
(denoted with the pound sign # and delimited by semicolon)
SubIndexAccess, bit-coded write-access authorization for individual components. Zero for write-authorization for all components.

## Slide 18: GW Script -- example
//--------------------------------------------
// Transducer Block 0
// Analog Input Transducer Block
//--------------------------------------------
BLOCK_INFORMATION Block=TB0 Tag=POSITIONER_TB BlockType=PTB ExecutionTime=0 DD_Rev=1 Profile_Rev=1 Start_index=START_INDEX_TR_BLK0 StartIndVIEWS=START_INDEX_VIEWS_TBLK0 NrVIEW3=1 NrVIEW4=1
#include "positioner_tb.gw"
// index = 14
STANDARD_PARAM FINAL_VALUE RW 5 Record FLOAT_S 2 #0;0.0 SubIndexAccess=0
// index = 15
STANDARD_PARAM FINAL_POSITION_VALUE RW 5 Record FLOAT_S 2 #0;0.0 SubIndexAccess=0
.........................................
// index = 18
PARAM FIND_STOPS RW 4 Simple INTEGER32 1 #0
.........................................
// index = 20
PARAM SUPPLY_PRESSURE R 5 Record FLOAT_S 2 #0;0.0 SubIndexAccess=0
// index = 21
PARAM ACTUATOR_PRESSURE R 5 Record FLOAT_S 2 #0;0.0 SubIndexAccess=0
END_BLOCK

## Slide 19: FW Source Code Changes
File for modifications:
<...\FD-SW\target\appl\fdev\src\appl_ptb.c>
4 spots in the file to modify:
The function < Appl_handle_HART_cmd()>;
The function < Write_handler_PTB() >;
Two lists: /* Cyclic commands */ and /* Regular commands */
Definition segment with “pound-defined”
- command numbers
- macros like CMD_..._FINAL_VALUE_OFFSET
Each HART command is a “case” statement of the “switch”, which makes the body of the funtion appl_handle_HART_cmd()
Each FF parameter is a macro in the “case”:
WRITE_HART_CMD and READ_HART_CMD

## Slide 20: Cyclic and Non-cyclic Parameters (commands)
Cyclic Parameters:
  /* Cyclic commands */ --
  high priority (frequent)
  /* Regular commands */ --
  low priority (less frequent)
Non-cyclic Parameters:
Write_handler_PTB() – explicit calls to:
appl_send_acyc_HART_cmd()

## Slide 21: FW Source Code Changes (sample)
case CMD_154_READ_SETPOINT:
{
if ( access == RECEIVE )
{
/* read FINAL_VALUE from HART */
READ_HART_CMD(CMD_154_FINAL_VALUE_OFFSET, p_PTB->final_value.value , FLOAT);
p_PTB->final_value.status = SQ_GOOD_CAS | SUB_NON_SPECIFIC;
}
else if ( access == SEND )
{
*send_length = HART_READ_CMD_REQ_LEN ;
}
break;
} /* end case CMD_154_READ_SETPOINT */

## Slide 22: FW Source Code Changes (sample continued)
case CMD_155_WRITE_SETPOINT:
{
if ( access == RECEIVE )
{
/* read FINAL_VALUE from HART */
/* there is no data to read */
}
else if ( access == SEND )
{
WRITE_HART_CMD(CMD_155_FINAL_VALUE_OFFSET, SPSubCmd, USIGN8);
WRITE_HART_CMD(CMD_155_FINAL_VALUE_OFFSET + 1, p_PTB->final_value.value, FLOAT);
WRITE_HART_CMD(CMD_155_FINAL_VALUE_OFFSET + 5, SPmode, USIGN8);
*send_length = CMD_155_REQUEST_LENGTH ;
}
break;
} /* end case CMD_155_WRITE_SETPOINT */